Start Slide
Introducing the Arduino Uno
(wiring, programming and running
a cute traffic light simulation)
Presented by Dave Mawdsley,
DACS Member, Linux SIG Member

---
The Arduino Microcontroller
1
The Arduino Uno Microcontroller

---
Installing Software Packages
2
Installing Software Packages
Ubuntu 10.04 LTS (without 'arduino' package)
* download and install the latest release and install with Archive Manager:
aduino-0022.gtz
* install the compiler (gcc-avr) and the libraries (avr-libc) packages:
sudo apt-get install gcc-avr avr-libc
* if you use the USB port to dialog, you should add yourself to the
group 'dialout' in order to have write permissions on that port:
sudo usermod -aG dialout madmod

---
Selecting the Arduino Board
3
Selecting the Arduino Board

---
The Arduino IDE With Code Sketch
The Arduino IDE With Sketch Code
4

---
Uploading Bytecode to the Board
5
Uploading Bytecode to the Board
After a successful
compilation, the
bytecode needs
to be uploaded
to the board.
Connect the USB
cable and upload.
Once uploaded,
the program can
be closed and
the computer
disconnected.

---
Traffic Light Schematic
6
Traffic Light Schematic

---
Traffic Light Program p1 of 3
7
Traffic Light Program p1 of 3

---
Traffic Light Program p2 of 3
8
Traffic Light Program p2 of 3

---
Traffic Light Program p3 of 3
9
Traffic Light Program p3 of 3

---
Wiring - Arduino, Breadboard, 9-volt Battery
10
Wiring – Arduino, Breadboard, 9-volt Battery

---
All Wired and Connected to the Computer
11
All Wired and Connected to the Computer

---
Arduino Power Issues--Short Course
12
Arduino Power Issues–Short Course
When the USB cable is connected to a running computer, the Arduino board can get its power via the USB's 5 volts of DC power from the computer's system board. That power of 5 volts DC is mainly for the board itself with some reserve for running simple external boards that have very low power requirements. Each of the Arduino digital pins 2 – 13 can supply a maximum of 40 mA to devices it connects with which should be okay for switching, transistors, diodes, etc.
However, Arduino's external power connector additionally supports from 7-12 volts DC and is thus easy to use with a 9-volt battery. This power is intended for demands a bit beyond the board's 5-volt via USB and makes the board more stable.
When external devices are still more demanding such as motors and relays, the external board needs its own power supply at its required ratings. Power transistors in the digital circuits can make the task easier when the power demands between the board itself and the external equipment differs considerably.
In general, it's best to study the loading that devices running simultaneously will demand. Analog devices can create serious drains.

---
Notes About the Arduino C Language
13
Notes About the Arduino C Language
The Arduino Integrated Development Environment (IDE) allows for the creation of C-like programs which features particular structures that land up in bytecode being uploaded to the Arduino board. Once there the board can execute the code disconnected from the computer using the external power connector with a 9-volt battery.
The source code is not compiled into regular C object code that can be run from Terminal or a GUI. Regular C is missing lots of dependencies which are supplied by the Arduino IDE and require its environment.
By preference, the source code can be written with a regular text editor and opened inside the Arduino IDE when it's ready. (my preference) The Arduino IDE allows for attempts to create bytecode without the board connected and will display what errors it can detect at that stage.
The Arduino website at www.arduino.cc/ is very helpful with lots of community support.

---
Typical Coding for a Digital I/O Pin
14
Typical Coding for a Digital I/O Pin
int ledPin = 13;	// LED connected to digital pin 13
void setup()	// mandatory Arduino function
       {
pinMode(ledPin, OUTPUT);	// sets the digital pin as output
       }
void loop()	// main Arduino function
       {
  digitalWrite(ledPin, HIGH);	// sets the LED on
  delay(1000);	// waits for a second
  digitalWrite(ledPin, LOW);	// sets the LED off
  delay(2000);	// waits for two seconds
       }

---
End Slide
Introducing the Arduino Uno
(wiring, programming and running
a cute traffic light simulation)
This OpenOffice.org Presentation
'arduino.odp' can be downloaded from
 http://madmod.com/freebies.html