Start Slide
Infrared Communication with the Arduino Uno
(using an infrared keypad, infrared receiver and an Arduino Uno)
Presented by Dave Mawdsley,
DACS Member, Linux SIG Member
June 19, 2013

---
Basic Wiring Photo
1
Basic Wiring Photo
The picture shows the Arduino Uno and breadboard wiring. The breadboard contains three LED's (green, yellow, red), three 330 ohm resistors to protect them and the infrared sensor (black). Data input and output lines are green, +5V is red and ground is black.

---
The Breadboard-Arduino Configuration
The Breadboard-Arduino Configuration
2
Signal Lines green
Ground black
+5V red
Resistors: 330 Ω
Digital Data:
D12 – green LED
D11 – yellow LED
D10 – red LED

---
The Infrared Sensor Keypad
3
The Infrared Sensor Keypad
Keypad Keys Used and their Assignment:
Each LED when instructed will alternate: ON 1 second, OFF 1 second,
ON 1 second, OFF.
Keypad 1 Key	→	LED_green
Keypad 2 Key	→	LED_yellow
Keypad 3 Key	→	LED_red

---
Sequence to Light an LED
4
Sequence to Light an LED
 1. Press key 1, 2 or 3 on the keypad
 2. Send the pulse stream via the IR LED from the keypad to the IR
       receiver.
 3. Capture the pulse times in an array pulse[ ]
 4. Build an array of 32 bits bit[ ] corresponding to the long or short
       pulse times. bit[0] – bit[14] (keypad), bit[17] – bit[31] (key pressed)
 5. Compute the integer for the keypad manufacturer's 15-bit code.
 6. Test to see if the remote is the proper one.
 7. Compute the integer for the pressed key's 15-bit code.
 8. In the coding for the switch, select the proper case.
 9. Execute the commands of the case 30600.
10. Repeat step 1.

---
5
What a Keypress on the Remote Does
The remote I'm using is from DFRobot.com is “IR Kit For Arduino (DFR0107)” which includes an infrared receiver and a 21-key infrared keypad transmitter.
When a key such as “3” is pressed, the keypad sends a series of pulses that light up the IR LED. For this keypad, a keypress generates a 32-pulse stream. The short pulses of about 522 microseconds are each later interpreted and coded as binary bit 0, and with each longer pulse of about 1648 microseconds interpreted as binary bit 1. The transmitter only sends IR LED pulses to the IR receiver.
The 32-pulse stream of short or long pulses picked up by the IR receiver is then saved in an array of pulse times by the software running on the Arduino.
This transmission technique is called PWM or Pulse Wave Modulation and it is widely used in applications for industry to control signaling and motors. Your IR TV remote works this way.

---
How Successful is this Pulse Array?
6
How Successful is this Pulse Array?
The software running in the Arduino expects 32 pulse values as it next builds a bit array of 32 bits corresponding to the pulses. The values of the pulse times vary a little each time the button on the keypad is pressed.
The short ones have a mean of about 522 microseconds (μs) and only vary from 463 μs to 581 μs using 4 standard deviations from the mean on a sample. Pulse times outside that interval occur only about 6 times in 100,000 samples—very rarely.
The long ones have a mean of about 1648 μs and and only vary from 1626 μs to 1671 μs using 4 standard deviations from the mean. Pulse times outside that interval also occur only about 6 times in 100,000 samples.
The software displayed later uses a short pulse threshold of 450 μs and a long pulse threshold of 1500 μs making these values very safely below the actual pulses recorded.

---
What Do the Pulses Look Like?
7
What Do the Pulses Look Like?
The figure shows a typical portion of the pulse stream of 32 pulses from the keypad when a key is pressed. Four pulses are shown.

---
How is the Pulse Array Made?
8
How is the Pulse Array Made?
The pulse array of 32 values is constructed one pulse at a time with the pulseIn function. The pulse[i] array has the actual recorded times for the long and the short pulses. Long pulse times will later be assigned a bit value of 1 and short pulse times will get the bit value 0.
The IR_PIN goes LOW briefly between the pulse times and acts to separate them. pulseIn actually times the pulses and yields an integer in microseconds.
        (spaces added for clarity In this code)
        void read_pulse( int pulse[ ] ) {
        for ( int j = 0; j < 32; j++ ) {
        pulse[ j ] = pulseIn( IR_PIN, HIGH );
        }
        }

---
How is the Bit Array Made?
9
How is the Bit Array Made?
The pulse array is read one pulse at a time. Pulses > 1500 μs have the corresponding bit value of 1. Otherwise if the pulse > 450 μs, then the bit value is 0. If the pulse time <= 450 μs, the pulse time is invalid.
(spaces added for clarity In this code)
        void pulse_to_bits( int pulse[ ], int bits[ ] ) {
        for( int j = 0; j < 32; j++ ) {
        if( pulse[ j ] > 1500 ) {	// codes for a bit value of 1 bits[ j ] = 1;
        }
        else if( pulse[ j ] > 450 ) {	// codes for a bit value of 0
        bits[ j ] = 0;
        }
        else { }	// pulse value was invalid }
        }

---
Pulse and Bit Arrays for Key Press 1
10
Pulse and Bit Arrays for Key Press 1
Here's a sample keypad key press of 3:
pulse[ ] = [516 545 516 512 540 510 506 536 1645 1656 1648 1645 1649 1641 516 1648
        515 506 540 510 1645 516 512 547 1650 1654 1645 1641 547 1648 1650 1641]
The corresponding bit array is:
bit[ ] = [0 0 0 0 0 0 0 0 1 1 1 1 1 1 0 1 0 0 0 0 1 0 0 0 1 1 1 1 0 1 1 1]
The green 15-bit portion of the bit array codes the manufacturer's keypad identifier.
The red 15-bit portion of the bit array codes for particular keypad key 3 pressed.
The black 2-bit middle portion of the 32-bit array is ignored.

---
Computing Two Decimal Integers
11
Computing Two Decimal Integers
bit[ ] = [0 0 0 0 0 0 0 0 1 1 1 1 1 1 0 1 0 0 0 0 1 0 0 0 1 1 1 1 0 1 1 1]
First we'll deal with the green 15-bit portion of the array. The bits are arranged left to right from the least significant bit to the most significant bit. So the actual binary string is 0 1 1 1 1 1 1 0 0 0 0 0 0 0. Coding this back to a decimal integer
gives 16128 which is easy to test to see if it's the correct keypad.
Next we'll deal with the red 15-bit portion of the array. The bits are arranged left to right from the least significant bit to the most significant bit. So the actual binary string is 1 1 1 0 1 1 1 1 0 0 0 1 0 0 0. Coding this back to a decimal integer
gives 30600 which is easy to use in coding to turn on the red LED.

---
From Bits 0-14 to a Decimal Integer
From Bits 0-14 to a Decimal Integer
12
Using the bit array, the first 15 bits are numbered 0, 1, 2, … , 12, 13, 14.
        Bit[ ] = [0 0 0 0 0 0 0 0 1 1 1 1 1 1 0 1 0 0 0 0 1 0 0 0 1 1 1 1 0 1 1 1]
 This code fragment works to figure out the decimal integer for the manufacture's
 keypad starting with the least significant bit[0] to the most significant bit [14] .
        void RemoteVerify( int bits[ ] ) {
        int seed = 1;
        for( int j = 0 ; j < 15 ; j++ ) {
        if( bits[ j ] == 1 ) {
        result += seed;
        }
        seed *= 2;
        }
        if (remote_verify != result) { // Verify first 15 bits. delay for data stream to end, then try again.
        delay(60);
        get_ir_key(); // main function to get the pulse times, get the bits and compute the integer
        }
        }

---
13
From Bits 17-31 to a Decimal Integer
 This code works to figure out the decimal integer for the keypad keypress 3
 starting with the least significant bit[17] to the most significant bit [31] .
        int bits_to_int( int bits[ ] ) {
        int result = 0;
        int seed = 1;
        for( int j = 17 ; j < 32 ; j++ ) {
        If( bits[ j ] == 1 ) {
        result += seed;
        }
        seed *= 2;
        }
        return result;
        }

---
Using the Computed 30600 Value
14
Using the Computed 30600 Value
 void do_response(int key) { // key = result from bits_to_int function
        switch (key) {
        < Code Snipped >
        case 30600: // Remote Keypad Key 3 Flash red LED 2 times
        digitalWrite(led_red,HIGH);
        delay(1000);
        digitalWrite(led_red,LOW);
        delay(1000);
        digitalWrite(led_red,HIGH);
        delay(1000);
        digitalWrite(led_red,LOW);
        break;
        }
}

---
End Slide
Infrared Communication with the Arduino Uno
(using an infrared keypad, infrared receiver and an Arduino Uno)
This OpenOffice.org Presentation
'infrared.odp' can be downloaded from
http://madmod.com/freebies.html