Start Slide
Make the Raspberry Pi use GPIO
(interfacing the GPIO pins to the outside world)
Presented by Dave Mawdsley,
DACS Member, Linux SIG Member
September 18, 2013

---
Introduction
1
Introduction
Shown are views of the Raspberry Pi. Of particular interest in this presentation are the 26 pins that allow connections to outside devices. We'll study 9 of them.
26 pins – no labels on RPi
3.3V
Pin 1
SDHC 4GB
Card Slot –
Under the RPi

---
The T-Cobbler Breakout Kit
2
The T-Cobbler Breakout Kit
Because of the sensitivity of misconnecting the Raspberry Pi to the outside world, it is necessary to solder together the the Cobbler so that a ribbon cable can safely connect to the GPIO pins of the RPi. The red edge wire needs to be closest to the SDHC card when plugged into the RPi.
The Cobbler makes it safer and much easier to connect to the proper pins of the RPi via a breadboard connection. You'll need a soldering gun to connect the components. I used Radio Shack 60/40 Rosin-Core Solder with the solder diameter 0.032” suggested since the solder points are a close fit.
(Adafruit.com supplies a Cobbler unit versions for about $12.00, shipping included.
Shown is the Adafruit Pi T-Cobbler Breakout Kit for Raspberry Pi I decided to use.)

---
General Purpose Input/Output Pins (GPIO)
3
General Purpose Input/Output Pins (GPIO)
The figure arrows show the available pins for external access to the RPi.
Grayed out pins N/C are not for external connections--only for the RPi internally.
GPIO pins 17, 18, 21, 22, 23, 24, 25 are available for external I/O connections.
3.3V and GND are for the power and return via the Cobbler.
The 5V pin is marked in red as a caution since the RPi operates at the 3.3V level only. Incoming 5V signals must be voltage divided to yield only up to 3.3V before entering into the RPi.

---
Getting the Temperature from a Sensor
4
Getting the Temperature from a Sensor
The Plan:
  - Purchase a TMP36 temperature sensor. It can use 3.3V.
  - Mount it on a half-sized breadboard.
  - Connect it to the RPi
  - Write a Python program to process the sensor and yield information.
Issues: (pretty daunting for the novice)
  - The TMP36 yields an analog voltage between 0V and 3.3V but the RPi has
    only digital GPIO pins.
  - The analog voltage needs to be converted to a digital value from 0 to 1023 so an analog-to-digital (ADC) device needs to be found that uses 3.3V. The ADC MCP3008 will work just fine once the technical sheets can be found.
  - How should the RPi, MCP3008 and TMP36 wiring be done?
  - How should the Python program handle the data?

---
Purchase a TMP36
5
Purchase a TMP36
Adafruit (adafruit.com) sells a TMP36 for a complete price of $5.82. We can use a supply voltage for it from 2.7V to 5.5V, so 3.3V will work just fine.
The TMP36 has 3 pins:
  - Pin 1: 3.3V
  - Pin 2: Data Out
  - Pin 3: GND
    This is looking at the
    flat side that has the
    writing. The back
    is curved.

---
Install the TMP on a Breadboard
6
Install the TMP36 on a Breadboard
The figure shows a small breadboard.
Vertical pins on each red rail connect together and vertical
pins on each blue rail connect together.
5 pins oriented horizontally are connected together in each row.
So pins 1, 2 and 3 of the TMP36 are on different, unconnected rows.
We'll come back to the TMP36 later.
TMP36
1
2
3

---
Install the Cobbler & MCP3008 on the Breadboard
7
Install the Cobbler & MCP3008 on the Breadboard
I purchased the Cobbler Kit and the MCP3008 together for $21.99 from adafruit.com.
Cobbler uses pin rows 1-13
spanning each half of the
breadboard. (13 each side)
TMP36
1
2
3
The 16-pin MCP3008 uses
pin rows 23-30 (8 each side)

---
Wiring it all Together
8
Wiring it all Together
Here's how it all connects together with the RPi. On the breadboard itself, I use red for 3.3V, black for GND and green for all signal I/O lines. Colors here are for clarity.

---
The Assembled Breadboard with the RPi
9
The Assembed Breadboard with the RPi

---
Just a Few Explanations for Now
10
Just a Few Explanations for Now
The RPi is considered the Master and the MCP3008 is considered the Slave. This is a legacy from multiple drives on the same IDE cable of a computer. (Master/Slave jumpers)
MISO (Master In, Slave Out), MOSI (Master Out, Slave In) So the RPi has only one input, but has multiple outputs to control the slave.
CS (chip select) with a bar means digital 0 is active, digital 1 is inactive. CLK (clock) is active with digital 1 and inactive with digital 0. TMP36 sends analog voltage to CH0.

---
The Data Retrieval Sequence
11
The Data Retrieval Sequence
1. 3.3V and GND are applied to the whole circuit when the RPi starts. 2. The Python program assigns the GPIO pins as input or output. 3. It verifies a use of a channel such as CH0. 4. CS is sent a 0 to ready the MCP3008 and CLK with a 1 accepts the input from the TMP36 and converts the voltage to a 10-bit binary buffer with the voltage converted to a number from 0 to 1023. 5. MOSI sends a 1 to ask for a bit value and clocks it. MISO receives either a 1 or a 0 and the Python program builds a buffer on the RPi to copy what the MCP3008 buffer is holding. 6. The Python program repeats the process until the entire buffer is received. 7. The Python program then deselects the MCP3008 with a CS digital 0.
8. The Python program processes the 10-bit binary and converts it back to a temperature value which can then be displayed. (This bit manipulation is called Bit Banging.)

---
A Look at 10 Internal-Purpose Pins
12
A Look at 10 Internal-Purpose Pins
  Left Column of Pins
  0 SDA	Serial Data Line 0
  1 SCL	Serial Clock Line 1
  4	General Purpose Clock
  10 MOSI	Master Output Slave Input
  9 MISO	Master Input Slave Output
  11 SCKL	Serial Clock
  Right Column of Pins
  14 TXD	UART Transmit (TXD)
  15 RXD	UART Receive (RXD)
  8	Chip Select 0 (1st Slave)
  7	Chip Select 1 (2nd Slave)

---
Closing Remarks
13
Closing Remarks
The MCP3008 has 8 analog channels CH0 through CH7. Each can be used for a different analog input. Of course, the coding of the Python program requires that the proper channel be selected before clocking in a value. This means that each of the channels requires Bit Banging to properly use the MCP3008.
The internal operation of the MCP3008 uses operational amplifier circuits to convert the analog inputs into the 10-bit buffer that can be extracted. The MCP3008 does this automatically once the chip select has become active and a CLK signal is sent. The 10-bit buffer holds the bit values waiting for a MOSI signal to start sending the bits out. When completed via the MISO signals, another analog channel can be selected and the process of conversion and data retrieval repeated.
The RPi is well suited to its GPIO operations and the Python libraries have what is needed to manage the GPIO manipulations successfully.

---
End Slide
Make the Raspberry Pi use GPIO
(interfacing the GPIO pins to the outside world)
This OpenOffice.org Presentation
'raspgpio.odp' can be downloaded from
 http://madmod.com/freebies.html